Primitive Iterator 4-bit architecture
PI – the data-driven, lightweight computer architecture
_____________________________________________________

Developer’s Guide – Full Edition

0. Table of contents

0. Table of contents – page 1
1. PI architecture overwiew – page 1
2. Data and Flags – page 2
3. Instructions – page 3
4. Input and output operations – page 4

1. The data-driven architecture – PI architeture overview

What does it mean that this assembly is data-driven? It means that the programmer simply manipulates the data and moves it around – computer is the one conducting the operations.

What does it mean that this assembly is lightweight? It means that it will only take you a couple of minutes to read the full Developer’s Guide and get familiar with the architecture.

Core principles:

1. Simplicity – all CPU registers are co-addressed as memory, giving the programmer maximum wiggle room in manipulating the data, with just 2 simple assembly instructions.

2. Complexity on the programmer’s side – you, as the programmer are the best equipped to know how data should be manipulated by your code. That’s why there’s no complex multi-step instructions. there is no micro-code – PI assembly itself is essentially the micro-code. This way you have maximum control over what exactly is being done – isn’t this exactly what coding in assembly is about?

3. Speed – Every instruction takes one clock cycle and one clock cycle only.

Arthmetical-Logical Unit (ALU):

This most crucial element of the CPU conducts all Arthimetical and Logical operations.
In the 4-bit PI architecture CPU, the ALU has two 4-bit inputs and one 4-bit output.

The output is either an arithmetical sum of the two numbers given on input or NAND of all bits from the inputs. Output cannot be enabled or disabled. ALU is always listening to inputs and always transmitting it’s output.

Whenever ,,ALU input” and ,,ALU output” is mentioned in this document, it is referring to exactly those values.
ALU also always stores the carry bit from the last operation.
2. Data and Flags
All registers and memory cells are 4-bit wide.

Memory:

All CPU registers are co-addressed with memory. Meaning that they all can be accesed just like normal memory cells.

	Adress:	Annotation:
Registers	0000	00 registry – Instruction Pointer
	0001	01 registry - Alpha
	0010	10 registry - Beta
	0011	11 registry - Accumulator
Regular memory	0100
	…
	1110
	1111

As you may observe, 2 last bits of the adress correspond to the registry number.

Instruction Pointer (IP) – shows instruction that is currently being executed. 2 is added automatically after each instruction to this registry. IP can only store even numbers.

Alpha and Beta – two registers wired directly to the ALU at all times (always enabled).

Accumulator – hard wired to ALU, after each instruction in which Alpha or Beta are changed the Accumulator is automatically updated with ALU output.

Memory containing instructions shall always be aligned by 2. First 4 bits of the instruction are to be stored under an even address. Next 4 bits are to be stored in the next memory cell (with an odd adress). As shown below:

Adress:	Content:
XXX0	Instruction 1
XXX1
XXX0	Instruction 2
XXX1

Because all registers serve as memory, there is nothing preventing you from storing instructions inside registers.

Flags:

Flag number:	Flag name:	Description:
00	HF – Halt Flag	When the flag is set to 1, all activity of the CPU is stopped. When the flag is set to 0, CPU works normally.
01	SF – Skip Flag	When the flag is set to 1, all instructions are skipped, except instructions that would change the value of this flag. When the flag is set to 0 - all instructions are executed normally.
10	AF – ALU Flag	When the flag is set to 0, ALU output is sum of Alpha and Beta. Otherwise each bit of ALU output is NAND of respective bits of Alpha and Beta

3. Instructions
All instructions are 8-bit long, meaning they take 2 memory cells each.

MOV:
The most important and basic instruction of the PI assembly. It is used to move data from a registry to memory (or reverse). Note, that since all registers are co-addressed with memory – you can also move data between registers (MOV 0 01 0011 will move data from 11 registry to 01 registry)

0	R	REG	MEM
1 bit	1 bit	2 bits	4 bits
Instruction code	Reverse Flag	Registry number	Memory address

When R is 0, data is transferred from memory (MEM) to a regisry (REG). When R is 1, the direction is reversed.

FLAG:
This is an instruction, that serves to alter the control flow of the program, by changing flags (described on page 2).

1	FLAG	VALUE	CARRY	ACC	NEG	OP
1 bit	2 bits	1 bit	1 bit	1 bit	1 bit	1 bit
Instruction code	Flag number	Value inserted into the flag	Indicating if to include carry	Indicating if to include accumulator	If set to 1 – final value inserted into the flag will be negated	Indicating operation performed on the inputs (0 – OR, 1 - AND)

Flag indicated by the argument FLAG will be set.

Other arguments determine what will the input be.

VALUE is given directly to be put into the FLAG

CARRY and ACC indicate if Carry from the ALU (from the last operation) and logical sum (OR) of all bits in the Accumulator will be combined with the value given in argument VALUE.

OP indicates in what way all included values will be combined (AND / OR).

NEG gives the opportunity to negate the whole input (after including VALUE, CARRY and ACC, as well as conducting operation specified by OP)

4. Input and output operations

CPU and memory compliant with the PI architecture should provide 5 output pins and 10 input pins, that allow for communication with peripheal devices, external sensors, etc. as well as programming of the computer.

In general, PI CPU works in one of 2 availible modes: programming mode and running mode.

Pins are outlined below. As you can see, the programming mode allows you to directly alter all memory and registers. Meanwhile the running mode only allows data to be input into the Accumulator.

Size and type:	Name:	Operations in programming mode:	Operations in running mode:
1-bit input	Mode switch	Pin for switching between modes / 1 – running mode / 0 – programming mode
1-bit input	Input confirmation pin	Sets the memory cell specified by the Adress input to the value specifiec in the Data input	If Halt Flag equals 1, sets Accumulator to the value specified in Data input. Otherwise does nothing.
1-bit input	Resume pin	The behaviour is undefined.	0 – does nothing / 1 – Sets the Halt Flag to 0, if HF equals 0, then does nothing.
4-bit input	Address input	Wired directly to address bus	The behaviour is undefined.
4-bit input	Data input	Wired directly to the data bus.	Wired directly to Accumulator registry (0011 memory cell) input.
4-bit output	Data output	The behaviour is undefined.	Those pins are always set to the value of the Accumulator.
1-bit output	Halt indicator	The behaviour is undefined.	This pin is always set to the value of the HF